## Slide 1: Gearbox fundamentals for wind technicians
Fabrikam FGT-3200 in the Litware LT-32 - Yusuf Arkwell - October 2025
FICTIONAL - NOT FOR OPERATIONAL USE | Gearbox fundamentals - October 2025

## Slide 2: From rotor to generator
The gearbox raises 12.7 rpm at the rotor to 1,500 rpm at the generator.
FICTIONAL - NOT FOR OPERATIONAL USE | Gearbox fundamentals - October 2025

## Slide 3: Three stages
Planetary stage: planet carrier, three planet gears, ring gear and sun pinion
Two parallel helical stages
Overall ratio 1:118.4
Rotor 12.7 rpm, generator 1,500 rpm
FICTIONAL - NOT FOR OPERATIONAL USE | Gearbox fundamentals - October 2025

## Slide 4: Shaft names and acronyms
Acronym | Meaning
LSS | Low-speed shaft - main shaft on the rotor side
IMS | Intermediate-speed shaft - between the two helical stages
HSS | High-speed shaft - output shaft to the generator coupling
PQ index | Particle quantifier index - amount of ferrous debris in an oil sample
RMS | Root mean square - value used for vibration velocity
FICTIONAL - NOT FOR OPERATIONAL USE | Gearbox fundamentals - October 2025

## Slide 5: Lubrication: the change to PWG 220
Since SB-LWS-2025-07 our gearboxes use Proseware PWG 220 (ISO VG 220) instead of PWG 320
410 L per gearbox; 60 L flush during the conversion
Minimum oil temperature for start-up: +5 °C (it was +10 °C with PWG 320)
Never mix oils: top up with PWG 220 only
FICTIONAL - NOT FOR OPERATIONAL USE | Gearbox fundamentals - October 2025
Notes: The conversion campaign runs from September to November 2025 (MOC-2025-012).

## Slide 6: Temperatures and alarms
Normal oil sump temperature 50 to 65 °C
A2101 warning at 75 °C; A2102 trip at 82 °C
The thermostatic valve opens the cooler circuit at 45 °C
Keep the cooler fan and the radiator clean
FICTIONAL - NOT FOR OPERATIONAL USE | Gearbox fundamentals - October 2025

## Slide 7: Condition monitoring
Vibration velocity RMS on the HSS bearings: alert 3.5 mm/s, alarm 4.5 mm/s
Oil analysis every 6 months: iron alert 50 ppm, PQ index alert 60
The trend matters more than a single value
FICTIONAL - NOT FOR OPERATIONAL USE | Gearbox fundamentals - October 2025

## Slide 8: Typical failure modes
HSS bearing damage: spalling and axial cracks
Micropitting on gear teeth
Cooler fouling and fan motor failures
Oil leaks at seals and hoses
FICTIONAL - NOT FOR OPERATIONAL USE | Gearbox fundamentals - October 2025

## Slide 9: Exploded view of the FGT-3200
Item numbers as in the maintenance manual LWS-MM-GBX-32, figure 4-1.
FICTIONAL - NOT FOR OPERATIONAL USE | Gearbox fundamentals - October 2025

## Slide 10: Quiz
1. Which shaft drives the generator?
2. At which oil temperature does A2102 trip the turbine?
3. Which oil do we use since the conversion?
4. What does a rising PQ index tell you?
FICTIONAL - NOT FOR OPERATIONAL USE | Gearbox fundamentals - October 2025
Notes: Answers: 1. the HSS. 2. 82 °C. 3. Proseware PWG 220. 4. More ferrous wear debris, often from a bearing.