## Slide 1: Quellmoor Ridge Wind Farm - onboarding and site rules
Contoso Renewables - induction for new staff and contractors - February 2025
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025

## Slide 2: Welcome to Quellmoor Ridge
12 Litware LT-32 turbines in CCV configuration, WTG-01 to WTG-12, 38.4 MW
Commercial operation since 15 October 2019
Hub height 92 m, rotor diameter 118 m
Grid connection to City Power & Light at the Skelvane 132 kV substation
O&M building with workshop and stores at the site entrance
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025
Notes: Show the site layout plan on the wall of the meeting room.

## Slide 3: Who is who
Role | Name
Site Manager | Maren Ellingsby
O&M Supervisor | Dario Penwarden
HSE Coordinator | Greta Vollan
Reliability Engineer | Yusuf Arkwell
Stores and spare parts | Tomasz Lebrecht
Lead Wind Technician | Callum Rydings
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025

## Slide 4: Site rules
Speed limit 20 km/h on all site roads
Sign in and out at the O&M building
Two persons minimum for any turbine access - no lone working
Helmet, safety boots and high-visibility vest outside vehicles
Report every incident and near miss on the same day
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025

## Slide 5: Permits and isolation
Every job on a turbine needs a PTW signed by the issuer
Isolation follows SOP-LOTO-001 with a personal padlock and name tag
High-voltage switching only by authorised persons
The control room must always know who is in which turbine
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025

## Slide 6: Climbing and rescue
Follow SOP-WAH-003 for all work at height
Climbing allowed up to a 10-minute mean wind speed of 15 m/s; hub entry up to 12 m/s
A sealed rescue kit is kept in every nacelle - check the seal every day
Rescue target: casualty on the ground within 15 minutes
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025

## Slide 7: Weather and ice
Ice detection (alarm A7001) stops the turbine automatically
Keep 300 m away from a turbine with ice on the blades
No climbing when lightning is detected within 15 km
In cold weather work in pairs and take warm breaks in the vehicle
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025

## Slide 8: Emergency
Raise the alarm to the control room first
Muster point: O&M building car park
First aiders on every shift; defibrillator in the O&M building and in each service vehicle
Follow the site ERP
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025

## Slide 9: Acronyms we use
Acronym | Meaning
CCV | Cold Climate Version - LT-32 variant with gearbox oil heaters, low-temperature steel and heated sensors
PTW | Permit to work
LOTO | Lockout/tagout
MOC | Management of change
TBT | Toolbox talk
SPL | Single-point lesson
WTG | Wind turbine generator (our turbine numbers WTG-01 to WTG-12)
ERP | Emergency response plan
CMS | Condition monitoring system
SB | Service bulletin (issued by the turbine manufacturer)
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025
Notes: Ask the participants which acronyms they already know.

## Slide 10: Environment
The site has an environmental permit with conditions on noise, shadow flicker, ice and wildlife
Some turbines stop automatically for permit reasons - never override these stops
A spill kit is kept in every turbine
Report any spill immediately to the HSE Coordinator
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025

## Slide 11: Questions?
HSE Coordinator: Greta Vollan
E-mail: greta.vollan@contoso-renewables.example
Keep this induction record with your training file
FICTIONAL - NOT FOR OPERATIONAL USE | Quellmoor Ridge onboarding and site rules - February 2025